| Article No. 03-5-5 | AXLE - REAR AXLE SHAFT AND/OR AXLE BEARING PREMATURE WEAR - VEHICLES PRODUCED BEFORE 1/1/2003 ONLY |
| --- | --- |
| Publication Date: February 28, 2003 |

| FORD: | 2003 CROWN VICTORIA |
| --- | --- |
| LINCOLN: | 2003 TOWN CAR |
| MERCURY: | 2003 GRAND MARQUIS |

Article 02-25-3 is being republished in its entirety to update the model line coverage. ISSUE:

Some 2003 Town Car (except Limo and Hearse chassis), Crown Victoria and Grand Marquis vehicles produced before 1/1/2003, may exhibit rear axle shaft and/or axle bearing premature wear. This is caused by excessive load, temperature, and inadequate lubrication. 

ACTION:

To service, install Rear Axle Bearing Service Kit, Part Number 3W1Z-4A109-AA. Refer to the instruction sheet included with the service kit.

| PART NUMBER | PART NAME |
| --- | --- |
| 3W1Z-4A109-AA | Rear Axle Bearing Service Kit |

OTHER APPLICABLE ARTICLES:

NONE

SUPERSEDES:

02-25-3

WARRANTY STATUS:

Eligible Under The Provisions Of Bumper To Bumper Warranty Coverage

| OPERATION | DESCRIPTION | TIME |
| --- | --- | --- |
| 030505A | Install Axle Bearing Service Kit | 1.5 Hrs. |

DEALER CODING

| BASIC PART NO. | CONDITION CODE |
| --- | --- |
| 4234 | 42 |

OASIS CODES:

509000, 510000, 703200, 703300